FOR IMMEDIATE RELEASE

Auralex® Offers Hemisphere™ Model 180 3D Sound Diffusors

INFOCOMM, Orlando, FL, June 17, 2015 – Auralex® Acoustics, Inc. (booth 1472), the world’s leading brand of acoustical treatments, offers its Hemisphere™ Model 180 3D Sound Diffusors, which combine shape and high-impact hardness to diffuse sound evenly across the room to control “flutter & echo” effects. The Auralex Hemisphere is a great choice for tracking spaces, control rooms or any environment in need of control of sound reflections.

Hemisphere helps maintain a “live” sound and a 3D sense of openness to the room by randomly scattering mid-to-high frequencies to provide a pleasing listening experience. In addition to the standard fire-rated Hemisphere, custom versions are available with added absorption for additional control. Hemispheres are available in their natural textured white finish, and in two fabric finishes to match Auralex’s ProPanel series.

Auralex Hemisphere Features:

- Material: 0.125" Thermoformed Copolymer (recyclable)

- Optional Absorption: 1½", Thick Fiberglass Backing

- Sizes: 23" x 23" x 7" (Custom sizes available upon request)

- Mounting: Two-Part Clip System (not ceiling grid compatible)

- Finish/colors: Textured White or Optional Fabric Covering (Guilford Spinel Obsidian & Sandstone)

- Flammability: All components have a Class “A” rating per ASTM E84

For more information, please visit www.auralex.com.

Photo Files: Hemisphere_White.JPG, Hemisphere_Sandstone.JPG, Hemisphere_Obsidian.JPG

About Auralex® Acoustics, Inc.

Located in Indianapolis, Auralex® Acoustics was founded in 1977 with a mission to provide top-performing acoustical treatment products at the best possible value. Since then, thousands of satisfied Auralex customers have experienced improved acoustics, expert advice and exceptional customer service. Auralex products enjoy widespread use among prominent artists, producers, engineers, corporations, celebrities and government agencies worldwide.

Auralex Acoustics has become the industry leader in innovative sound control solutions and continues to enjoy rapid growth through an international network of authorized dealers. Visit the Auralex Web site at www.auralex.com. Auralex can be reached via email at auralexinfo@auralex.com or by calling 1-800-959-3343.

# # #

PR Contact Info:

Clyne Media, Inc.

615-662-1616

info@clynemedia.com

Auralex® Acoustics is exhibiting at booth 1472 at the 2015 InfoComm Convention in Orlando, Florida.