FOR IMMEDIATE RELEASE

The Spokane Arena Uses Focusrite’s RedNet to Put Its Audio on the Network

AV systems integrator Second Wind Productions installs five RedNet 1’s, one RedNet 2, seven RedNet MP8R’s and one RedNet D64R, creating a comprehensive networked ecosystem for the venue’s live and broadcast sound that brings a new level of routing flexibility and sonic clarity

Los Angeles, CA, June 13, 2016 – Like many modern sports and entertainment venues built in the last 25 years, the Spokane Veterans Memorial Arena in Spokane, Washington, was designed as a multi-purpose facility. In addition to serving as the home to the Spokane Chiefs of the Western Hockey League and starting this year the home of the Spokane Empire of the Indoor Football League, it’s also been the site of numerous top-tier concerts, in which case seating is expanded to over 12,000. A venue that needs to cover that many bases was having a difficult time with the aging audio networking system it had in place, but that audio system has now been transformed with the installation of RedNet components from Focusrite. The arena’s audio tech team, including Tech Specialists Monte Koch and Mike Sackville-West, were early adopters of networked audio, and the move to a Dante™-enabled system, including Focusrite RedNet components, was a natural fit.

AV systems integrator Second Wind Productions sold and integrated five RedNet 1 eight channel A-D/D-A interfaces, one RedNet 2 16-channel A-D/D-A interface, seven RedNet MP8R 8-channel remote-controlled mic pre’s, and one RedNet D64R MADI Bridge into a complete and coherent digital audio networking ecosystem. The RedNet 1 and RedNet 2 units act as I/Os for all rack-mounted audio systems in the arena, including audio from the instant replay and video-clip playback systems in the AV control room. These feed the large video displays in the venue. The RedNet MP8R is the gateway to the facility’s Dante™ audio-over-IP network; the RedNet D64R provides the link between a Dante Ethernet-based audio system and any MADI / AES10 setup, such as the Meyer Sound Galileo DSP used for the PA system.

Robert Duven, Owner of Second Wind Productions, says that the RedNet components were the best choice for a facility that pursues technical excellence. “Focusrite’s RedNet product line was a great choice for this project because it met several key criteria,” he explains. “First, it offered Dante-enabled endpoints with exceptional audio quality. Next was the availability of excellent engineering and tech support, both in the design phase and long-term for the client. And finally, it was equipment that would adapt easily as direct replacements for existing input/output devices.” He continues, “Spokane Arena’s audio team of Monte and Mike have always embraced the philosophy of updating and upgrading the facility. By employing proven new technologies, and as early users of networked audio systems, they realized the advantages of migrating to the Dante standard.”

The Arena had had experience with networked audio before, but in some respects it had fallen short of expectations. “The previous audio networking system worked, but to get customer service for problem resolution we had to call France,” explains Monte Koch. He contrasts that with the RedNet experience, noting that the system was assembled and up and running in less than a day, with customer service that is always just a quick phone call away, no matter the time zone.

“And RedNet was our path to a Dante network,” says his colleague, Mike Sackville-West. “We’re a 12,000-seat arena, and it was time to make that jump to Dante. Now, we can put a standard network switch anywhere and we’re ready to go.”

Sackville-West likes the fact that he and Koch — both grounded in audio — were able to move onto a network so easily and get audio from anywhere they need to on the network on the arena’s dedicated audio VLAN. “We have RedNet to thank for that,” he says. And for a new level of reliability, with Ethernet and power supply redundancy through RedNet. “This was really a leap into the future,” says Sackville-West. “And that’s where RedNet is going to keep taking us.”

Photo file: Focusrite_Spokane.JPG

Photo caption: Gear rack at Spokane Arena, featuring Focusrite RedNet components.

For further information, head to www.focusrite.com or contact:

USA: Hannah Bliss +1 (310) 322 5500 // Hannah.Bliss@focusrite.com

Robert Clyne  +1 (615) 662-1616 // robert@clynemedia.com

About Focusrite

The Focusrite brand was established in 1985 and the founding principles of the company were to develop products that sounded more musical, in addition to just measuring well – today, we still carry these founding principles forward in our class-leading and award-winning designs. We measure our success by the success of you, our clients, and you will find Focusrite product prominent in professional and project studios throughout the world. Based just outside of London, we work with the best design talent throughout the world to bring you the tools to enhance the way you work. Our product is made with pride and principle in a highly automated ISO 9002 factory with significant level of test by engineers who themselves are musicians and understand the part our product plays in your process.