FOR IMMEDIATE RELEASE

Press Contact:						Company Contact:

Leslie Buttonow						Rebecca Eaddy

Account Manager					Marketing Communications Mgr.

Clyne Media, Inc.						Roland Corporation U.S.

(615) 662-1616						(323) 890-3718

Leslie@clynemedia.com 					Rebecca.Eaddy@roland.com

## Roland Introduces SE-02 Analog Synthesizer

## Roland and Studio Electronics collaborate on debut of Roland Boutique Designer Series

Los Angeles, CA, June 20, 2017 — Roland introduces the SE-02 Analog Synthesizer, a collaborative effort from Roland and Studio Electronics, and the debut product of the new Roland Boutique Designer Series. Featuring authentic discrete analog circuitry and hands-on controls for nearly every function, the compact SE-02 allows users to produce classic and modern sounds with vast programmability.

The SE-02's analog synth engine features three voltage-controlled oscillators, a 24 dB low-pass filter, and a dual gain-stage amplifier. The oscillators have six different waveforms with the warmth and complex character associated with true analog VCOs. In addition, the oscillators are temperature stabilized with automatic tuning to provide solid operation while performing.

Other features include three types of cross modulation (XMOD), a filter feedback loop, a tempo-syncing LFO with nine waveforms, envelope sweeping and inverting, oscillator sync, a noise generator, and a tempo-syncing delay. The SE-02 comes equipped with 384 preset sounds that cover a wide range of classic and modern tones. With the large selection of panel controls, users can modify presets or create all-new sounds and store them in 128 available user locations.

The SE-02 also includes a 16-step sequencer that can sync to external tempo via MIDI, USB, or trigger input. Per-step gate time, adjustable glide, tempo, and patch number are stored with each sequence, and it’s possible to adjust shuffle, scale, direction, and first/last steps on the fly. Parameters can be automated by pressing a step and moving a control. Users can store 128 sequence patterns and construct 16 songs, each with up to 16 parts.

The SE-02 features standard MIDI jacks for connecting any MIDI keyboard controller. Trigger I/O and CV inputs for pitch and filter frequency allow the SE-02 to work with modular setups and other vintage gear. Routing external audio signals through the filter section is possible, while USB audio/MIDI support provides integration with computer-based setups.

To learn more about the SE-02 Analog Synthesizer, visit www.Roland.com.

---------

Photo file 1: Roland_SE-02_Straight.JPG

Photo caption 1: Roland SE-02 Analog Synthesizer

Photo file 2: Roland_SE-02_Angled.JPG

Photo caption 2: Roland SE-02 Analog Synthesizer

For high-resolution images of these products, please visit our press and dealer resources center and visit here for embeddable videos.

About Roland Corporation

Roland Corporation is a leading manufacturer and distributor of electronic musical instruments, including keyboards and synthesizers, guitar products, electronic percussion, digital recording equipment, amplifiers, audio processors, and multimedia products. With more than 40 years of musical instrument development, Roland sets the standard in music technology for the world to follow. For more information, visit www.Roland.com or see your local Roland dealer.

About Studio Electronics

Studio Electronics is a leader in excellence and ingenuity in analog synthesizer design since 1988. Makers of the revered MidiMini, SE-1, ATC-1, Omega 8, CODE 8, Boomstar, and Tonestar, Studio Electronics produces premium-quality musical instruments, hand-built in the USA. For more information, visit www.studioelectronics.com.