NEWS RELEASE

Contact: Clyne Media, Inc.

Tel: (615) 662-1616

Fax: (615) 662-1636

FOR IMMEDIATE RELEASE

AUDIO-TECHNICA UNVEILS THE U851RO OMNIDIRECTIONAL CONDENSER BOUNDARY MICROPHONE

STOW, OH, February 15, 2011 — Audio-Technica brings to market the new U851RO Omnidirectional Condenser Boundary Microphone. Featuring breakthrough audio and mechanical design innovations, the phantom-powered U851RO offers outstanding speech intelligibility and transparent sound quality for surface-mount applications. Such applications include high-quality sound reinforcement, professional recording, television, conferencing and other demanding sound pickup situations.

The U851RO’s small-diameter UniPoint® capsule near the boundary eliminates phase distortion and delivers clear, high-output performance. The unit is equipped with a PivotPoint® rotating output connector, allowing the cable to exit from either the rear or the bottom of the microphone; a UniSteep® filter, which provides a steep low-frequency attenuation to improve sound pickup without affecting voice quality; and UniGuard® RFI-shielding technology, which offers outstanding rejection of radio frequency interference. Self-contained electronics eliminate the need for an external power module. It accepts interchangeable condenser elements in cardioid and hypercardioid polar patterns.

The U851RO features a low-profile design with a low-reflectance black finish for minimum visibility, in addition to a heavy die-cast case and silicon foam bottom pads to help minimize coupling of surface vibration to the microphone. The U851RO’s low-profile element provides a uniform omnidirectional polar pattern with a 360-degree acceptance angle.

U851RO Specifications:

Element		 		Fixed-charge back plate, permanently polarized condenser

Polar Pattern		 		Omnidirectional in hemisphere above mounting surface

Frequency Response 		30-20,000 Hz

Low Frequency Roll-Off 		80 Hz, 18 dB/octave

Open Circuit Sensitivity 		-31 dB (28.2 mV) re 1V at 1 Pa

Impedance		 		200 ohms

Maximum Input Sound Level 	132 dB SPL, 1 kHz at 1% T.H.D.

Dynamic Range (typical) 		111 dB, 1 kHz at Max SPL

Signal-to-Noise Ratio	 	73 dB, 1 kHz at 1 Pa

Phantom Power Requirements 	11-52V DC, 4 mA typical

Switch				 	Flat, roll-off

Weight				9.2 oz (262 g)

Dimensions	 			4.25" (108.0 mm) maximum length,

3.31" (84.0 mm) maximum width,

0.91" (23.0 mm) maximum height

Output Connector		 	TB3M-type

Cable				 	25' (7.6 m) long, 0.13" (3.2 mm) diameter, 2-conductor,

shielded cable with TA3F-type and XLRM-type connectors

Optional Interchangeable Elements 	UE-C cardioid (120°); UE-H hypercardioid (100°)

Accessory Furnished	 	Soft protective pouch

The U851RO Omnidirectional Condenser Boundary Microphone is currently available with a U.S. MSRP of $313.00. For more information, please visit www.audio-technica.com.

…ends 357 words

Photo Files: U851RO.JPG

Click here for U851RO product profile and downloadable high-res photo(s).

See more Audio-Technica news releases.

Celebrating over 45 years of audio excellence worldwide, Audio-Technica is a leading innovator in transducer technology, renowned for the design and manufacture of microphones, wireless microphones, headphones, mixers, and electronics for the audio industry.

—For more information on the complete range of Audio-Technica products, contact

Karen Emerson, Audio-Technica U.S., Inc., 1221 Commerce Drive, Stow, OH 44224.

Tel: (330) 686-2600; Fax: (330) 688-3752; Web: www.audio-technica.com

—For further information regarding product availability and pricing in the United Kingdom, please contact Harvey Roberts (hroberts@audio-technica.co.uk); in Germany, please contact Anja Groth (a.groth@audio-technica.de); in the rest of Europe, please contact Evangéline Pirot (epirot@audio-technica-europe.com).