PRESS RELEASE

Contact: Clyne Media, Inc.

Tel: (615) 662-1616

Fax: (615) 662-1636

FOR IMMEDIATE RELEASE

Genelec Debuts F One and F Two Active Subwoofers

CEDIA EXPO, DENVER, CO, September 26, 2013 — As part of its new offerings, Genelec (booth 508) is displaying its new F Series Active Subwoofers at CEDIA 2013. Consisting of the F One (6" active) and F Two (8" active) subwoofers, the F Series units are designed to be used separately or to complement the new Genelec G Series of active two-way loudspeakers, which includes four models. The F One and F Two feature elegant industrial design by award-winning designer Harri Koskinen and Genelec’s R&D team.

Genelec’s F Series active subwoofers are designed to complement G Series loudspeakers in applications where an extended and powerful reproduction of very low frequencies is required. The all-metal construction of the subwoofers hides the driver and connectors on the bottom, leaving the clean form of the enclosure undisturbed. Both models feature connections and bass management for up to 5.1 channels and a comprehensive suite of adjustments for perfect matching to the main loudspeakers and room acoustics.

F One Specifications:

- Maximum sound pressure: 98 dB @ 1 m

- Frequency response: 35 - 85/120 Hz (± 3 dB)

- Phase correcting: 0 to -270° (90°/step)

- Driver: 6 1/2”

- Amplifier power: 40 W

- Dimensions: Height x Diameter 9.88" x 12.01" (251 x 305 mm)

- Weight: 13.89 lb (6.3 kg)

F Two Specifications:

- Maximum sound pressure: 102 dB @ 1 m

- Frequency response: 27 - 85/120 Hz ± 3 dB

- Phase correcting: 0 - 270° (90° steps)

- Driver: 8”

- Amplifier power: 150 W

- Dimensions: Height x Diameter 11.81" x 14.25" (300 x 362 mm)

- Weight: 21.61 lb (9.8 kg)

For more information, please visit www.genelecusa.com.

...ends 258 words

Photo File: F_One_Black.JPG, F_Two_White.JPG

Genelec, the pioneer in Active Monitoring technology, is celebrating its 35th anniversary of designing and manufacturing active loudspeakers for true and accurate sound reproduction. Genelec is credited with promoting the concept of active transducer technology, which many manufacturers are just now incorporating into their products. Since its inception in 1978, Genelec has concentrated its efforts and resources into creating active monitors with unparalleled sonic integrity. The result is an active Custom Installation speaker system that has earned global acclaim for its accurate imaging, extremely high acoustic output from small enclosures, true high-fidelity with low distortion, and deep, rich bass.

Other company and product names may be trademarks of the respective companies with which they are associated.

—For more information on the complete range of Genelec Custom Installation Systems, please contact: Genelec Inc., 7 Tech Circle, Natick, MA 01760. Tel: (508) 652-0900;

Fax: (508) 652-0909; Web: www.genelecusa.com.

Genelec is exhibiting at booth 508 at the 2013 CEDIA Expo in Denver, Colorado.