-FOR IMMEDIATE RELEASE-

Carl Tatz Design Announces Two New Professional Near-Field Monitors

New PhantomFocus™ PFM HD and UHD-1000 series monitors define current state of the art in near-field monitoring

Nashville, TN: Carl Tatz Design® LLC (CTD™), the award-winning studio and monitoring design firm, has announced two new professional near-field reference monitors as part of its line of acclaimed PhantomFocus™ Precision Monitoring Instruments.

The PFM HD-1000 High Definition and the PFM UHD-1000 Ultra-High Definition Professional Monitors are intended for audio professionals demanding the highest performance in dedicated mix room or control room/tracking installations. Designed to be used exclusively in tandem with CTD's acclaimed on-site installed PhantomFocus System, both monitors offer superb vocal rendition, the ability to handle high SPLs (115dB continuous) with lightning-fast transient response, articulate detail and PhantomFocus’s trademark sonically holographic pinpoint imaging at all listening levels.

The PFM HD-1000 is a passive near-field monitor in a low-profile D'Appolito design facilitating console/listener placement. With accelerated response time, phase linearity and tightly controlled mid-bass response, the PFM HD-1000 reveals effortless power, accuracy and non-fatiguing performance beyond that of traditional high- and mid-frequency driver motor capability. It features two proprietary Morel® 5.63-inch (143.51 mm) “Uniflow™” aluminum diecast woofers with large 3-inch voice coils and a proprietary 1-inch (23.4 mm) ScanSpeak high-frequency tweeter with patented phase plug design. The monitor is available with the passive Straight Wire™ crossover and an optional bi-amp version. The PFM HD-1000 Monitor dimensions are HWD 8.2" x 17.8" x 12.2" (208.28 mm x 452.12 mm x 309.88 mm), and it weighs 22.2 lbs. (10.06 kg).

The flagship PFM UHD-1000 is offered only in a bi-amp configuration and shares all the inherent qualities of the PFM HD-1000 Monitor, while its powerful bi-amplified configuration and woofer complement, considered to be amongst the finest in the world, introduces a depth of field and articulate sonic command heretofore unknown in a professional near-field monitor, enhancing performance, power and headroom, and expanding on its effortless non-fatiguing precision character. Using the same ScanSpeak® tweeter as the HD-1000, it is distinguished by its high-end ScanSpeak dual 5.5-inch (139.7 mm) proprietary woofer complement, adding increased depth, speed and articulate sonic authority. The PFM UHD-1000 Monitor dimensions are HWD 8.2" x 17.8" x 12.2" (208.28 mm x 452.12 mm x 309.88 mm), and it weighs 24.1 lbs. (10.93 kg).

Both models feature a unique self-bracing trapezoidal cabinet with internal cross-bracing and tuned damping, and a pro-industry-first custom-integrated pistonic decoupling system from IsoAcoustics®.

Both monitors and recommended amplification are now available at www.phantomfocus.com, along with full specifications.

Photo file 1: PFM_HD-1000.JPG

Photo caption 1: PhantomFocus™ PFM HD-1000 Professional Monitor

Photo file 2: PFM_UHD-1000.JPG

Photo caption 2: PhantomFocus™ PFM UHD-1000 Professional Monitor

Photo file 3: IsoAcoustics.JPG

Photo caption 3: IsoAcoustics® integrated pistonic decoupling system

Photo file 4: PhantomFocus_Brochure.PDF

About Carl Tatz Design

Carl Tatz Design (CTD) is an award winning studio design firm offering design and consulting services to homeowners and entertainment industry professionals in areas of: Recording Studios, Monitor Systems, Home Screening Rooms, Dedicated Listening Rooms, Acoustic Analysis, Tuning, and Sound Isolation. Carl Tatz is also the inventor of the industry acclaimed proprietary PhantomFocus™ System (PFS™) monitor tuning protocol. CTD’s many resources combine knowledge, experience and expertise in sound, picture and design to serve its clients worldwide. For more information, visit http://www.carltatzdesign.com.

About the PhantomFocus™ System

Carl Tatz Design’s proprietary PhantomFocus™ System monitor tuning protocol offers clients a unique opportunity to have a truly world-class monitoring experience in their room, no matter how modest. All speakers interact with the room they’re in, and the PhantomFocus System allows any monitors to perform at maximum accuracy - in any room - with a full 20Hz-to-20KHz frequency response and pinpoint imaging in what some owners have described as a “holographic sweet spot.” It is a new level of sonic accuracy that engenders easier, better and faster mixing that translates well in any environment.

There are approximately fifty steps in the proprietary PhantomFocus System implementation protocol, including phase alignment, system damping, speaker decoupling and isolation mounting, careful assessment of engineer/speaker placement relative to primary axial room modes, proprietary laser-calibrated speaker distancing and angle alignments, digitally-controlled crossover points and slopes for pass filtering, and, proprietary, multiband parametric equalization.

Hardware solutions can include monitor stands, concrete, Sorbothane™ and other isolation and damping materials, custom floating plenum mounts, subwoofer systems and custom digital processors. The PhantomFocus System evaluation and implementation is a full two-day process and can be applied to near-fields, mid-fields, and large soffit mounted monitors, regardless of manufacturer.

Carl Tatz Design installs the PhantomFocus System in existing control rooms and in all studios that are designed and built from the ground up by CTD. The result is like the aural equivalent of HD TV. Once you experience a PhantomFocus System, you can’t go back.

About the Carl Tatz Signature Series™ by Auralex®

The Carl Tatz Signature Series™ by Auralex® family of control room acoustic modules (now featured in a dedicated section on the Auralex website), emulates the look and acoustics of Carl Tatz's custom designs at a fraction of the cost.

When paired with the acclaimed PhantomFocus System, it becomes the CTD MixRoom™, the sonic performance of which is unrivaled anywhere, defining a new standard for the audio professional. The MixRoom can quickly and affordably transform a simple rectangular room into a world-class mixing environment without peer.

"We're honored to work with Carl Tatz, one of the top studio designers in the industry, on this exciting new Auralex offering. This new series makes Carl's signature style easy and affordable enough for any serious studio owner. Now virtually any room can benefit from the same aesthetic and sound control enjoyed by top hitmakers like Rascal Flatts and others," says Eric Smith, founder and president of Auralex Acoustics.

For more information about Carl Tatz Design LLC and the PhantomFocus™ System, please contact Carl Tatz Design, 6666 Brookmont Terrace, Suite #1109, Nashville, TN 37205 Office: 615.354.6242, Direct: 615.400.5479

Email: carl@carltatzdesign.com

Web: www.carltatzdesign.com

Store: www.phantomfocus.com